## PART 1. GENERAL

  - INTRODUCTION

Supply and fix Luxalon( Lay-In Stretch Metal Tile Ceiling System as manufactured by Hunter Douglas Architectural Products.

  - DESCRIPTION OF THE SYSTEM

The system will consist of metal tiles laid into a 15 mm, 24 mm slotted tee bar system or

50mm or 100mm Bandraster system.

## PART 2. PRODUCT

  - STRETCH METAL TILES

________m2 Luxalon( Lay-in Stretch Metal Tile Ceiling consisting of:

Square edged tiles which are 585x585 mm (T15), 575x575 mm (T24) both module 600 x 600 or 595 x 595 mm (bandraster 50) with module 625 x 625 or 900 x 900 mm (bandraster 100) with module 920 x 920 made of 1.0 mm thick steel or aluminium. The square edged tiles are designed to lay recessed 10 mm or 15 mm below the level of the tee bar or lay in flush with the tee bar/bandraster.

  - SUSPENSION

Consists of pre-punched main tee sections installed in a grid by means of inserting cross tees which are designed to be used with the size of tile selected.

or

Consists of main bandraster sections installed in a grid by means of inserting cross bandraster profiles which are designed to be used with the size of tile selected.

Maximum distance of rapid hangers fixing points on the main tee is 1200 mm. Main tees and cross tees will be finished standard baked white enamel finish. Matching colours to the tiles are available on request.

## PART 3: ADDITIONAL SPECIFICATIONS

  - EDGE COVER PROFILES

- L-profile 25  x  25 mm made of 1.5 mm thick steel

- W-profile 25 x 25 x 8 mm made of 1.5  thick steel

- F-profile, 35 x 40 mm, made of 1.5 thick steel

- L profile angled, 40 x 30 mm(12° angle), made of 1.5 thick steel

  - MESH TYPES

Manufacturer shall supply all Stretch Metal Lay-in tiles with the following aluminium or steel mesh types:

- LD6, open area 23 %

- LS6, open area 38 %

- LS8, open area 62 %

- LS10, open area 68 %

- LS12, open area 72 %

- LS 16, open area 66 %

  - ACOUSTICS

Manufacturer shall supply acoustic pads white/black to put on top of the stretch metal tiles,  thickness___mm density____kg/m3 and of a size completely fill the tile.

  - COATING

Architect will make a colour selection from the RAL colour range for Luxalon( Stretch Metal Tiles RAL code no._______or a special colour will be made to match.

The coating will consist of a tough and durable polyester powder coating finish, electro statically applied onto electro-galvanized steel or aluminium, phosphatised and chemically treated according to high industrial standards (DIN 1541/ TAIM standards).

  - INSTALLATION

All materials shall be installed in strict compliance with all local codes, ordinances and manufacturers recommendations including specific additional requirements as may be called for in the specifications or shown on the drawings.

  - SUBSTITUTIONS

Ceiling installers wishing to submit proposals on systems other than the Luxalon Stretch Metal Tile Ceiling System shall, at least 10 days in advance of the bid date, submit to the architect complete descriptive information of the total system concept and performance data tests made as a system. In addition include a list of similar installations of the proposed substitution. If approval is made an addendum will be issued enumerating such approved system as herein set forth.