| Product: | Hunter Douglas® Sun Louvre System 70S |
| --- | --- |
| System: | Fixed system, vertical applications |
| Shape: | Z-shaped panels with backrolled rounded edges |
| Panel section: | 70S: 47.5 x 70 mm, thickness 0.6 mm |
| Panel length: | max. 6000 mm |
| Alloy: | EN-AW 3005 |
| Surface treatment: | Frontside: Luxacote® finish, 3 layer, 40 mµ, colours; see colour chart Backside: polyester coating, standard white |
| Panel fixing: | Panel bracket for 70S extruded, anodised aluminium |
| Spacers: | 48, 63 and 88 mm extruded, anodised aluminium spacers for different panel modules |
| Panel modules 70S: | Spacer Module Shadow angle: 43 mm 70 mm 0° 63 mm 85 mm 19° 88 mm 110 mm 44° |
| Support fixation: | Support fixed to façade by means of hot dip galvanised steel console, with extra aluminium top brace as an option |
| Support system: | Aluminium extruded supporting rail for panels and spacers |
| Rail support: | Railclamp with washer set |
| Fixing: | Clip system |
| Installation: | Spacers and panel brackets are sliding into support rail which is fixed with rail clamp to substructure (not Hunter Douglas® program) |